## Slide 1: Noble Gas Monitoring for Nuclear Accident Forensics
Steven Biegalski, Ph.D., P.E.
Nuclear and Radiological Engineering and Medical Physics

## Slide 2: Outline
Noble Gasses
Detection Network
Radioxenon Forensic Signatures
Fukushima
Conclusions

## Slide 3: Noble Gasses
The main noble gases of interest for CTBT monitoring include isotopes of xenon and radon.
Noble gasses have advantages for forensic measurements because:
  They are more likely to leak from a reactor or underground test than other elements.
  Minimal chemical reactions in environment to perturb forensic signature.
  Creation at source can be relatively high.

## Slide 4: Radioxenon
Noble gasses are important for nuclear monitoring as they may not be easily filtered or contained
Xenon is a noble gas whose isotopes are produced in high yield from nuclear fission.
Argon is largely produced from activation.
This talk will largely focus on radioxenon within the context of monitoring for the Comprehensive Nuclear-Test-Ban Treaty (CTBT).
http://en.wikipedia.org/wiki/File:ThermalFissionYield.svg

## Slide 5: Radioxenon (cont.)
Xenon gas is present in Earth’s atmosphere at a concentration of 0.087±0.001 parts per million.
Radioxenon may be produced through either activation or fission.
http://atom.kaeri.re.kr/

## Slide 6: Radioxenon (cont.)
The four main radioxenon fission products of interest include 131mXe, 133mXe, 133Xe, and 135Xe.
They have good half-lives, production rates, and decay characteristics.
 | 131mXe | 133mXe | 133Xe | 135Xe
Half-Life | 11.9 days | 2.19 days | 5.24 days | 9.09 hours
235U Fission Yield Per 100 Fissions |  |  |  | 
Direct (%) – Thermal | 3.48 x 10-7 | 1.89 x 10-3 | 6.66 x 10-4 | 7.85 x 10-2
Direct (%) – Fast | 2.41 x 10-7 | 4.23 x 10-3 | 1.45 x 10-3 | 1.20 x 10-1
Cumulative (%) – Thermal | 4.05 x 10-2 | 1.95 x 10-1 | 6.70 | 6.54
Cumulative (%) - Fast | 4.51 x 10-2 | 6.72 | 1.98 x 10-1 | 6.60

## Slide 7: Radioxenon (cont.)

## Slide 8: Radioxenon Sources
Type of Release | Order of Magnitude Radioxenon Released
Hospitals | ~ 106 Bq/day/facility
Nuclear Power Plants | ~ 109 Bq/day/facility
Radiopharmaceutical Facilities | ~ 1011 to 1013 Bq/day/facility
Nuclear explosion underground | ~ 0 to 1015 Bq/kton
Nuclear explosion atmospheric | ~ 1016 Bq/kton
Saey, J. Environmental Radioactivity, 100, 396-406 (2009).

## Slide 9: Radioargon
The radioisotopes of argon are also of interest for nuclear monitoring.
Radioargon isotopes are primarily produced through activation processes.
Some half-lives suitable for monitoring.
Isotope | Half-Life | Notes
37Ar | 35.04 days | Produced primarily through 40Ca(n,α)47Ar with secondary production through 36Ar(n,γ) 37Ar reaction.
39Ar | 269 years | Produced primarily through 38Ar(n,γ) 39Ar with secondary production through 42Ca(n,α)49Ar reaction.
41Ar | 1.8 hr | Produced primarily through 40Ar(n,γ)41Ar. Short half-life does not facilitate regional monitoring.
42Ar | 32.9 years | Produced from double neutron capture 40Ar(n,γ) 41Ar(n,γ)42Ar with secondary production from 44Ca(n,γ)45Ca (n,α)42Ar. Low anticipated production.

## Slide 10: 37Ar World Background in Soil Air

## Slide 11: Surface Activity
Haas DA, HS Miley, JL Orrell, CE Aalseth, TW Bowyer, JC Hayes, JI McIntyre, “The Science Case for 37Ar as a Monitor for Underground Nuclear Explosions,” PNNL Document PNNL-19458, 2010.

## Slide 12: Detection Network
The Comprehensive Nuclear-Test-Ban Treaty (CTBT) defines an International Monitoring System (IMS).
The IMS consists of monitoring stations for:
  Seismic
  Infrasound
  Hydroacoustic
  Radionuclide

## Slide 13: Detection Network (cont.)
Radionuclide detection consists of:
  Particulate monitoring
  Noble gas monitoring
Radioxnon is the predominant noble gas being measured.
Radioargon technology is still at an infant stage.
http://ctbto.org/map/

## Slide 14: Radioxenon Forensic Signatures
Information may be determined about the source of radioxenon based on the content of the sample measured.
The more information you have, the better job you can do on a forensic analysis.
Other factors may also be utilized including:
  Station history
  Atmospheric Transport
  Knowledge of local sources
  Other measurements within IMS
    Radionuclide measurements
    Wave-form measurements

## Slide 15: Radioxenon Forensic Signatures
At the time of CTBT signature in 1996, just the presence of 135Xe in a sample was indicative of a nuclear weapon test.
Now system detection limits have improved to a point where some stations routinely see 135Xe.
From Perkins and Casey ‘Radioxenons: Their Role in Monitoring a Comprehensive Test Ban Treaty,’
prepared by Pacific Northwest National Laboratory, June 1996, DOE/RL-96-51

## Slide 16: Radioxenon Forensic Signatures
The first step for isotopic ratios showed promise to distinguish between commercial reactor emissions and nuclear explosions.
From Perkins and Casey, ‘Radioxenons: Their Role in Monitoring a Comprehensive Test Ban Treaty,’ prepared by PNNL, June 1996, DOE/RL-96-51.
Decay Time (day)
Decay Time (day)

## Slide 17: Radioxenon Forensic Signatures
The field has expanded to multivariate analysis techniques and multi-isotope ratio correlation (MIRC) plots.
This is basically a plot of ratios vs. ratios.

## Slide 18: Radioxenon Forensic Signatures

## Slide 19: Radioxenon Signature 235U vs 239 Pu

## Slide 20: Commercial Reactors
There are 437 operating commercial reactors in the world today.
Most are thermal reactors operating 12 to 18 months between refueling.
Radioxenon releases from these facilities are measured.
http://nuclearinfo.net/Nuclearpower/CurrentReactors

## Slide 21: Commercial Reactors

## Slide 22: Research Reactors
There are many designs of research reactors around the world.
Radioxenon emissions are more from air activation than from fission due to neutron beam lines and other irradiation facilities.
The University of Texas TRIGA Reactor

## Slide 23: Air Activation – Research Reactors

## Slide 24: Underground Nuclear Test Signatures
The radioxenon source signature at the time of production is well established.
The Undergound Transport of Environmental Xenon (UTEX) code was developed to calculate the perturbations resulting during the process of radioxenon traveling to the surface.
Significant On-Site Inspection implications.
http://www.notpurfect.com/travel/nuke/nevada.html

## Slide 25: UTEX Sensitivity Study
JD Lowrey, S.R. Biegalski, AG Osborne, MR Deinert,” Subsurface mass transport alters the radioxenon signatures that are used to identify clandestine nuclear tests,” Geophysical Research Letters, 40, 1-5, 2013..
Editor’s Choice in Science (vol. 339, 18 Jan. 2013)

## Slide 26: Radiopharmaceutical Production
Radiopharmacutical production via 235U target activation is a major anthropogenic source of radioxenon in the atmosphere.
Major production facilities include:
  ANSTO, Australia
  CNEA, Argentina
  CRL, Canada
  IRE, Belgium
  NRG, The Netherlands
  NTP, South Africa
http://www.nuclearfaq.ca/cnf_sectionB.htm

## Slide 27: Medical Isotope Production - 99Mo
 | ANSTO | CNEA | CRL | IRE | NRG | NTP | Average
Al |  | 16.5 | 36 | 30 | 26.46 |  | 27.24
235U | 2.5 | 1.4 | 2.23 | 4.2 | 5 | 7.15 | 3.75
Flux | 9.0E+13 | 1.5E+14 | 2.5E+14 | 1.5E+14 | 1.5E+14 | 1.5E+14 | 1.6E+14
Min Irradiation (hr) | 72 | 72 | 150 | 100 | 144 | 50 | 155.5
Max Irradiation (hr) | 336 | 168 | 280 | 150 | 144 | 200 | 
Cooling (hr) | 11.5 |  |  | 36 | 20 | 112 | 44.875
Values from Saey , Bowyer, Ringbom, Applied Radiation and Isotopes, 68 (2010) 1846-1854

## Slide 28: Nominal Medical Isotope Signature
Direct Overlap
of Signatures

## Slide 29: Fukushima Nuclear Accident
Radioxenon was instrumental in determining the accident severity for the 2011 nuclear accident at Fukushima Daiichi.
Radioxenon was detected in the United States within three days of the accident.
Radioxenon measurements provided the first confirmation of significant core damage in all three reactors that were operating at the time of the earthquake.

## Slide 30
http://forecast.chapman.edu/japan.php
Note: This is just to
give you an idea. More
accurate plume models
have been generated
that show quicker
advancement of the plume
and wider diffusion.

## Slide 31: Fukushima (cont.)
First detections of 133Xe were made starting early March 16 in Richland, WA, USA, only four days following the earthquake.
Maximum concentrations of 133Xe were in excess of 40 Bq/m3, which is more than 40,000 the average concentration of this isotope is this part of the United States.
T.W. Bowyer, S.R. Biegalski, M. Cooper, P.W. Eslinger, D. Haas, J.C. Hayes, H.S. Miley, D.J. Storm, V. Woods, “Elevated Radioxenon Detected Remotely Following the Fukushima Nuclear Accident.” Journal of Environmental Radioactivity, 102(7), 681-687, 2011.

## Slide 32: Fukushima (cont.)
Radioxenon isotopes were measured at all US IMS stations equipped with noble gas monitoring equipment.
133Xe atmospheric activity concentrations measured
at the Ashland, KS,Charlottesville, VA, Wake Island, US, and Oahu,HI stations.
After initial release, decreasing trend matched the half-life of 133Xe showing no further major releases into the atmosphere.
Time series of 133Xe atmospheric activity concentrations for Ashland, KS, Charlottesville, VA, Wake Island, US, and Oahu, HI from March 11, 2011 to April 11, 2011.
S.R. Biegalski, TW Bowyer, P Eslinger, JA Friese, LR Greenwood, DA Haas, JC Hayes, I. Hoffman, M Keillor, HS Miley, M. Moring, “Analysis of Data from Sensitive U.S. Monitoring Stations for the Fukushima Daiichi Nuclear Reactor Accident,” Journal of Environmental Radioactivity, 114, 15-21, 2012.

## Slide 33: Fukushima
133Xe/131mXe isotopic activity ratio matched modeling of Fukushima reactor as a function of time.
Variation from station to station was attributed to calibration differences.
133Xe/131mXe isotopic activity ratio for US IMS stations (1 s error bars).
S.R. Biegalski, TW Bowyer, P Eslinger, JA Friese, LR Greenwood, DA Haas, JC Hayes, I. Hoffman, M Keillor, HS Miley, M. Moring, “Analysis of Data from Sensitive U.S. Monitoring Stations for the Fukushima Daiichi Nuclear Reactor Accident,” Journal of Environmental Radioactivity, 114, 15-21, 2012.

## Slide 34: Unit 1, 2, and 3 Xe Inventories
T.W. Bowyer, S.R. Biegalski, M. Cooper, P.W. Eslinger, D. Haas, J.C. Hayes, H.S. Miley, D.J. Storm, V. Woods, “Elevated Radioxenon Detected Remotely Following the Fukushima Nuclear Accident.” Journal of Environmental Radioactivity, 102(7), 681-687, 2011.

## Slide 35: Fukushima
Modeled dilution factors at five different detection locations were combined with 57 atmospheric concentration measurements of 133Xe taken from March 18 to March 23 to estimate the source term.
This analysis suggests that 92% of the 1.24 1019 Bq of 133Xe present in the three operating reactors at the time of the earthquake was released to the atmosphere over a 3 d period.
Preliminary results roughly one week after the accident showed 85% to 103% of radioxenon inventory was released from the three reactors providing early confirmation of core damage.
These result show how radioxenon measurements show the extent of core damage in a nuclear accident scenario.
P.W. Eslinger, T.W. Bowyer, M.W. Cooper, D.A. Haas, J.C. Hayes, H.S. Miley, J.P. Rishel, V.T. Woods, S.R. Biegalski, I. Hoffman, E. Korpach, J. Yi, K. Ungar, and B. White,” Source term estimation of radioxenon released from the Fukushima Dai-ichi nuclear reactors using measured air concentrations and atmospheric transport modeling,” Journal of Environmental Radioactivity, 127, 127-132, 2014.

## Slide 36: Conclusions
Radioxenon measurements may be a useful tool for the detection of nuclear events.
Detection sensitivity has significantly improved, so forensic signatures are necessary to identify sources.
Radioxeon is also useful to aid response efforts to nuclear events.